## Slide 1
PROJECT OVERVIEW
Dual-Rocket SoC
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
01
Evidence: CONFIGURATION.md | SOC.md
Configuration, architecture
and verification
Two 64-bit RISC-V cores. One shared-memory SoC.
Built from pinned Chipyard sources and evaluated
with open-source tools.
HART 0
Rocket + FPU
Private I/D caches
HART 1
Rocket + FPU
Private I/D caches
SHARED SYSTEM
512 KiB L2 + memory fabric
Boot, debug, interrupts, UART
Prepared for sainadh812 | 08 September 2026
Scope: generated RTL and exploratory mapping. No fabricated chip or physical signoff.
Notes: This presentation explains an existing Chipyard-generated dual-Rocket design and the recorded verification work. It is not a silicon product announcement. Created on 2026-09-08 from the September 6 evidence; no EDA or functional simulation was rerun to prepare these slides. All diagrams are logical illustrations, not physical layouts.
Evidence references (relative to project root unless URL):
docs/dual-rocket/CONFIGURATION.md
docs/dual-rocket/SOC.md
docs/dual-rocket/reports/simulation/README.md
docs/dual-rocket/reports/synthesis/README.md

## Slide 2
PURPOSE
What does this SoC do?
A SoC combines processors, memory infrastructure and system services.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
02
Evidence: SOC.md | reports/simulation/README.md
COMPUTE
Two instruction streams
Integer and floating-point work
SHARE DATA
Caches and coherent interconnect
Memory and atomic operations
CONTROL
Boot, interrupts, UART
External memory and debug
Demonstrated in simulation
RISC-V ISA programs and scalar benchmarks
Both-hart output, shared data and atomic updates
Not yet demonstrated
Custom firmware and multicore applications;
OS bring-up needs its own software and tests.
This is a development and verification platform, not a complete board-ready computer.
Notes: Each Rocket hart executes software instructions. The shared coherent hierarchy permits coordinated access to memory, while UART, interrupts and debug provide system services. The demonstrated use is bare-metal RTL simulation. Sv39 and privilege modes are present, but Linux boot was not tested. Application examples are categories of use, not benchmark performance claims.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/reports/simulation/README.md

## Slide 3
PROCESS
How the project was built
The work changed the selected configuration and tooling, not the generated CPU RTL.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
03
Evidence: CONFIGURATION.md | scripts/dual-rocket/README.md
01
PIN
Record source revisions
and tool versions
02
SELECT
Choose the existing
DualRocketConfig
03
GENERATE
Elaborate the full SoC
and emit RTL + metadata
04
VERIFY
Run RTL simulation,
lint and synthesis
05
REPORT
Preserve outcomes,
limits and input hashes
Configuration and SoC documented before fresh lint/synthesis; simulation predates those reruns.
Recorded evidence includes unsuccessful attempts and warnings, not only the passing summaries.
Notes: The selected DualRocketConfig already existed upstream. Generation used a prepared, pinned checkout and cached generator JARs. A simulation campaign completed before the documentation-driven lint and synthesis reruns. Configuration and SoC documentation were completed before those fresh reruns. Report packaging preserves failed attempts, diagnostics and provenance. The final generation-wrapper test used an up-to-date cache, not a new elaboration.
Evidence references (relative to project root unless URL):
docs/dual-rocket/CONFIGURATION.md
scripts/dual-rocket/README.md
docs/dual-rocket/reports/workflow/README.md
docs/dual-rocket/reports/simulation/README.md

## Slide 4
CONFIGURATION
The exact two-core configuration
Chipyard already provides this class; no hand-duplication of a Rocket core was needed.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
04
Evidence: CONFIGURATION.md
class DualRocketConfig extends Config(
new freechips.rocketchip.rocket.WithNHugeCores(2) ++
new chipyard.config.AbstractConfig)
SINGLE-CORE BASELINE
RocketConfig uses WithNHugeCores(1).
SELECTED DESIGN
DualRocketConfig uses WithNHugeCores(2).
The second hart shares the system fabric and L2; this is not two independent SoCs.
Notes: The CDE configuration composition searches leftmost fragments first; it is parameter composition, not concatenated RTL. WithNHugeCores(2) creates two tile parameter entries and updates NumTiles. AbstractConfig supplies the surrounding SoC; by itself it has no tiles. Huge names an upstream parameter preset and does not measure performance. Private L1 instances are duplicated and the shared directory width changes for the second coherent client.
Evidence references (relative to project root unless URL):
docs/dual-rocket/CONFIGURATION.md
https://github.com/ucb-bar/chipyard/blob/e602d917dcc495c58cabe906535e411707096c9c/generators/chipyard/src/main/scala/config/RocketConfigs.scala#L11-L17
https://github.com/chipsalliance/rocket-chip/blob/55bcad0f59436de98ea510334121de8546b9e9d7/src/main/scala/rocket/Configs.scala#L15-L60

## Slide 5
GENERATION
From Scala to generated hardware
The configuration is a recipe. Chipyard elaborates that recipe into RTL.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
05
Evidence: CONFIGURATION.md | artifacts/rtl.sha256
Scala + CDE
Select parameters
Chisel
Elaborate + negotiate
FIRRTL
Intermediate design
firtool
Lower + split RTL
Generated outputs
Split Verilog / SystemVerilog
DTS, memory map, L2 metadata
Memory interfaces and test selections
476
generated RTL source files
Snapshot includes simulation resources.
Only the selected hierarchy is analyzed.
RTL generation and simulator compilation are separate make targets.
Notes: chipyard.Generator selects chipyard.harness.TestHarness, containing ChipTop and DigitalTop. Chisel elaborates the design and Diplomacy negotiates buses, devices and clocks. FIRRTL and annotations are lowered by CIRCT firtool. The recorded options include --repl-seq-mem, --split-verilog and --export-module-hierarchy. Logical memory interfaces are not foundry SRAM selections. The 476-file manifest includes simulation resources and is not an instantiated DUT-module count. The native simulator is a separate build target.
Evidence references (relative to project root unless URL):
docs/dual-rocket/CONFIGURATION.md
docs/dual-rocket/artifacts/rtl.sha256

## Slide 6
ARCHITECTURE
Inside the full ChipTop SoC
Simplified functional grouping; individual bus adapters and control branches are omitted.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
06
Evidence: SOC.md | artifacts/chipyard.harness.TestHarness.DualRocketConfig.l2.json
ChipTop / DigitalTop
ROCKET TILE 0
RV64 + FPU
32 KiB I$ + 32 KiB D$
ROCKET TILE 1
RV64 + FPU
32 KiB I$ + 32 KiB D$
TileLink SBUS
CBUS / PBUS control path
SHARED L2
512 KiB inclusive cache
SYSTEM SERVICES
Boot / debug / IRQ / UART
MBUS
64 KiB scratchpad
AXI4 MEMORY
256 MiB window
64-bit data
Outside ChipTop
Other ports:
UART and JTAG
Serial TileLink
Clock and reset
Notes: Core data/instruction requests enter the TileLink system bus. The shared inclusive L2 connects SBUS to MBUS. The control-side path is SBUS to CBUS to PBUS, and serial ingress uses FBUS. The services box groups functions for readability and is not an assertion that all services attach to PBUS. Scratchpad is instantiated despite DTS disabled status. External memory is beyond the ChipTop boundary; the AXI window does not imply an on-chip DRAM controller or PHY. This is a logical diagram, not a floorplan; 64-bit AXI describes data width, not address width.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/artifacts/chipyard.harness.TestHarness.DualRocketConfig.l2.json

## Slide 7
PROCESSORS
What each Rocket tile contains
Hart 0 and hart 1 use the same core preset and private L1 geometry.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
07
Evidence: SOC.md
RESOURCE
PER-HART CONFIGURATION
Execution
RV64, in-order, single-instruction decode / retirement
Arithmetic
I/M/A/C + Zba/Zbb/Zbs; floating point F/D/Zfh
Privilege and MMU
Machine / supervisor / user modes; Sv39 virtual memory
Instruction cache
32 KiB, 8 ways, 64 sets, 64-byte lines
Data cache
32 KiB, 8 ways; blocking cache (nMSHRs = 0)
Protection and TLBs
8 PMP entries; 32-entry instruction and data TLBs
Not selected: vector V, Zbc carry-less multiply, or Zicboz cache-block zero.
Notes: The emitted DTS and pinned Rocket configuration confirm these properties. The generated ISA string includes b, but this must not be read as every bit-manipulation extension; Zba/Zbb/Zbs are explicitly selected, not Zbc. Single-instruction decode and retirement are in-order. FPU support includes F, D and Zfh. No V extension is selected. Cache capacities exclude metadata and padding. DTS CPU frequency fields are zero; no achieved CPU frequency is claimed.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
https://github.com/chipsalliance/rocket-chip/blob/55bcad0f59436de98ea510334121de8546b9e9d7/src/main/scala/rocket/Configs.scala#L15-L60

## Slide 8
MEMORY
The memory hierarchy
Architectural capacities are different from mapped SRAM bits and library cell area.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
08
Evidence: SOC.md | reports/synthesis/README.md
PRIVATE L1
128 KiB total
32 KiB I$ + 32 KiB D$ per hart
SHARED L2
512 KiB
Inclusive, 8-way, one coherence bank
SCRATCHPAD
64 KiB
On-chip at 0x08000000; DTS disabled
MAIN MEMORY
256 MiB window
External AXI4 region at 0x80000000
External main memory is not on-chip DRAM. ChipTop has no DDR controller or DDR PHY.
Notes: Each hart has 32 KiB instruction and 32 KiB data L1 caches, giving 128 KiB total across two harts. Shared L2 is 512 KiB, eight-way, 1024 sets, 64-byte lines, one coherence bank and seven MSHRs. The 64 KiB scratchpad exists in RTL but its device-tree status is disabled; software must account for that. The external window is 256 MiB at 0x80000000 and needs an external AXI memory subsystem. There is no DDR controller/PHY or 256 MiB on-chip memory.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/reports/synthesis/README.md

## Slide 9
SYSTEM SERVICES
Boot, peripherals and external interfaces
The base SoC includes essential control and debug, not every optional Chipyard device.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
09
Evidence: SOC.md | CONFIGURATION.md
BOOT + INTERRUPTS
Boot ROM / boot selection
CLINT timer + software IRQ
PLIC: UART device interrupt
EXTERNAL INTERFACES
UART RX/TX and JTAG
AXI4 external memory
Serial TileLink; clocks/reset
NOT IN THIS CONFIG
FFT / RoCC / vector unit
GPIO, I2C, SPI flash
Ethernet or DDR controller
Do we have FFT?
No dedicated FFT hardware. A Rocket CPU can execute FFT software;
an FFT accelerator needs a new integration and its own verification.
Optional generator code in Chipyard does not mean that block exists in this generated SoC.
Notes: CLINT provides timer/software interrupts to both harts. PLIC has one device source (UART) and four M/S interrupt contexts across two physical harts. JTAG debug supports system-bus access. Boot ROM has a 64 KiB address window, not necessarily 64 KiB of program bytes. ChipTop exposes external clocks and reset; the clock generator is passthrough, not a PLL. Decoupled serial TileLink uses 32-bit phits/flits; it is not UART. The current SoC has no FFT or other RoCC accelerator.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/CONFIGURATION.md

## Slide 10
MEMORY MAP
Key software-visible address regions
Addresses come from the emitted memory map and device tree.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
10
Evidence: SOC.md | artifacts/chipyard.harness.TestHarness.DualRocketConfig.memmap.json
BASE ADDRESS
WINDOW
RESOURCE / PURPOSE
0x00000000
4 KiB
Debug module
0x00010000
64 KiB
Boot ROM address window
0x02000000
64 KiB
CLINT: timer / software interrupts
0x02010000
4 KiB
Shared L2 control registers
0x08000000
64 KiB
On-chip scratchpad
0x0c000000
64 MiB
PLIC register aperture
0x10020000
4 KiB
UART registers
0x80000000
256 MiB
External main-memory window
Register-window size is not storage capacity. Full address table is in SOC.md.
Notes: This slide is a selected address map, not all 12 regions. The full map also contains boot-address, error-response, tile-gating and tile-reset windows. End addresses in the source report are inclusive. Register windows are address apertures, not RAM capacity. Scratchpad status is disabled in DTS despite being instantiated. PLIC's 64 MiB aperture is not 64 MiB of interrupt storage. Debug is at zero, not ordinary RAM.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/artifacts/chipyard.harness.TestHarness.DualRocketConfig.memmap.json

## Slide 11
MULTICORE BEHAVIOR
How two cores cooperate
Separate instruction streams can coordinate through shared memory and atomic operations.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
11
Evidence: SOC.md | reports/simulation/README.md
HART 0
Runs its own software
Publishes / checks shared data
SHARED STATE
Coherent memory
Atomic counter updates
HART 1
Runs its own software
Publishes / checks peer data
2 harts
required by explicit smoke
256
total atomic increments
PASS
peer-data visibility checked
Software must use both harts; two cores do not automatically make every program parallel.
Notes: This diagram is conceptual, not the instruction-by-instruction sequence of the test. The explicit two-hart atomic smoke requires both harts, peer-data visibility and a total of 256 atomic increments. Two-hart hello requires two hart-identifying outputs. Corrected multicore tests aggregate both hart results before success. Most physical ISA tests park the second hart; ordinary benchmarks can use one-hart startup code. Shared coherent caches do not automatically parallelize a program and atomic checks are not exhaustive coherence verification.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/reports/simulation/README.md

## Slide 12
SCOPE
Hardware boundary vs simulation harness
Full-SoC synthesis means ChipTop, not the whole simulated environment.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
12
Evidence: SOC.md | reports/simulation/README.md
TestDriver / TestHarness: simulation environment
ChipTop / DigitalTop
Both Rocket tiles, L1s and L2
Scratchpad, buses and peripherals
Clock/reset logic and I/O cells
EXTERNAL TEST MODELS
DRAMSim2 / simulated memory
SimJTAG, serial host, UART output
Test clocks and fast ELF loading
Synthesis boundary = ChipTop. +loadmem is a simulation shortcut, not fabricated hardware.
Notes: TestDriver and TestHarness instantiate the complete ChipTop plus test infrastructure. Simulation uses original behavioral memories and DRAMSim2. +loadmem writes the simulator memory model to load a program; it is not a hardware memory-write port. Simulated JTAG, serial host, UART output and clock sources are not ASIC hardware. Lint/synthesis select the ChipTop hierarchy. Lint uses original behavioral memories; synthesis applies validated SRAM adapters. RTL simulation does not validate the mapped netlist.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/reports/simulation/README.md
docs/dual-rocket/reports/lint/README.md
docs/dual-rocket/reports/synthesis/README.md

## Slide 13
VERIFICATION STRATEGY
Three checks answer different questions
Common source evidence; separate methods, outputs and acceptance boundaries.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
13
Evidence: reports/simulation/README.md | reports/lint/README.md
SIMULATION
Does this test execute?
Verilator + DRAMSim2
RISC-V programs and multicore tests
Reference checks with Spike
LINT
What does static analysis flag?
Verilator + slang
Full-ChipTop diagnostics
Warning baseline and source checks
SYNTHESIS
Can the design be mapped?
Yosys / slang + ABC
SRAM adapters and libraries
OpenROAD netlist linking
All three are useful. None alone establishes functional completeness or manufacturing readiness.
Notes: The completed software simulation campaign predates the fresh documentation-driven lint and synthesis runs. Lint and synthesis can run independently against the same preserved generated source snapshot. Their dates and artifacts are retained separately. Simulation asks whether specific tests execute successfully. Lint checks static diagnostics, not full behavior. Synthesis checks mapping and linkability into libraries, not physical signoff. 476 hashes refer to a full generated-source inventory, not 476 DUT instances.
Evidence references (relative to project root unless URL):
docs/dual-rocket/reports/simulation/README.md
docs/dual-rocket/reports/lint/README.md
docs/dual-rocket/reports/synthesis/README.md
scripts/dual-rocket/README.md

## Slide 14
RESULTS | SIMULATION
Simulation: configured tests passed
Recorded full-SoC RTL campaign, completed 06 September 2026. Not rerun for this deck.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
14
Evidence: reports/simulation/README.md | reports/simulation/summary.json
335 / 335
configured ISA tests
12 / 12
configured benchmarks
Broader inventory: 422 unique programs / variants
391 reported PASS
25 FAIL
6 wall timeouts
The expanded inventory did not pass completely. Do not report 422/422 passing.
Notes: All 335 configured ISA and 12 configured benchmarks passed. The configured ISA suite is a subset of the 349-program ISA inventory. The entire broadened campaign contains 422 unique programs/variants, with 391 reported PASS, 25 FAIL and six host wall timeouts. Retries are not added to the unique total. PASS results for some legacy programs carry oracle caveats explained on the next slide and in the report. Verilator simulation version is 5.022, distinct from the newer lint executable. Fast ELF loading bypassed serial program transfer.
Evidence references (relative to project root unless URL):
docs/dual-rocket/reports/simulation/README.md
docs/dual-rocket/reports/simulation/summary.json

## Slide 15
RESULTS | SIMULATION
Interpreting failures, timeouts and passes
Test intent and the correctness of the test itself matter.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
15
Evidence: reports/simulation/README.md | reports/simulation/reference-comparison/summary.json
9 ISA NON-PASSES
Additional unsupported-feature or
misaligned-access expectation probes
22 LEGACY NON-PASSES
Matrix geometry / test-oracle defects;
32 x 32 assumptions vs 16 x 16 data
Some reported legacy passes also have bounds or result-checking caveats.
Three corrected multicore supplements passed both RTL and Spike.
Spike agreed on 391 PASS and 31 non-PASS classifications.
Agreement with Spike is supporting evidence, not formal equivalence or exhaustive verification.
Notes: Nine non-passing additional ISA probes concern unsupported Zbc/Zicboz or misaligned-data expectations. They are not failures of the configured 335-test subset. The 22 legacy non-passes have 32-by-32 matrix assumptions against a 16-by-16 dataset; some reported legacy passes also have bounds or two-hart result-aggregation defects. Three separately named corrected multicore supplements passed RTL and Spike; original results remain preserved. Matched Spike has 391 PASS/PASS and 31 non-PASS/non-PASS outcomes, not identical exit behavior or cycle-level equivalence. The six final timeouts are host wall limits, not six proven core deadlocks. PMP passed after a bounded extended retry, and a C++ hello parser issue was corrected.
Evidence references (relative to project root unless URL):
docs/dual-rocket/reports/simulation/README.md
docs/dual-rocket/reports/simulation/reference-comparison/summary.json

## Slide 16
RESULTS | LINT
Lint: zero errors, warnings retained
Both tools analyzed full ChipTop using the original behavioral memories.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
16
Evidence: reports/lint/README.md | reports/lint/evidence/summary.json
TOOL
ERRORS
WARNINGS
NOTES
Verilator 5.051
0
2,484
0
slang 11.0.448
0
21
21
Dominant baseline
2,047 unused-signal warnings
424 empty pin connections
Review items still visible
4 reset-related SYNCASYNCNET warnings
1 clock-gate latch; 21 shift expressions
Zero errors is not warning-free signoff. Dedicated CDC/RDC review remains necessary.
Notes: Fresh wrappers started both lint tools at 2026-09-06T13:19:52Z. Verilator 5.051 reported 2484 warnings; slang 11.0.448 reported 21 arith-in-shift warnings and 21 notes. Both tool and wrapper exits are zero. All warning-category deltas are zero against the earlier DualRocketConfig baseline, not the historical one-core report. Verilator -Wno-fatal retains warnings but allows completion. No generated RTL edits or new suppressions were introduced. Four SYNCASYNCNET warnings require reset/clock review. EICG_wrapper's latch is consistent with an intentional clock-gate latch, not physical signoff. 419 source files are in slang's elaborated dependencies; the shared 476-file fingerprint is the full generated inventory.
Evidence references (relative to project root unless URL):
docs/dual-rocket/reports/lint/README.md
docs/dual-rocket/reports/lint/evidence/summary.json

## Slide 17
IMPLEMENTATION FLOW
How full-SoC synthesis was performed
Yosys performs synthesis and mapping; OpenROAD checks the mapped netlist can link.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
17
Evidence: reports/synthesis/README.md | scripts/dual-rocket/synthesis/README.md
01
Validate RTL + SRAM inventory
Check dimensions, masks, instances and source hashes.
02
Check SRAM adapters
Compare generated memory behavior over seven interfaces.
03
Synthesize and technology-map
Yosys + slang + ABC; Nangate45 / fakeram45 libraries.
04
Link and audit the result
OpenROAD reads all mapped instances; recheck inputs.
Technology mapping completed. No timing constraint, floorplan, placement or routing was run.
Notes: The flow preserves original RTL and uses an independent output directory. It checks full-ChipTop reachability and SRAM metadata; validates replacement adapters against behavioral memories; reads SystemVerilog with the slang Yosys plugin; maps logic with Yosys/ABC into Nangate45 cells and SRAM into fakeram45 macros; rejects unresolved cells/memories/processes; and links the complete mapped netlist in OpenROAD with Liberty/LEF. The first attempt failed because literal quotes reached Slang filename arguments, after SRAM tests. Relative input symlinks fixed the tooling issue and the full run was repeated. OpenROAD linking was not placement, routing or static timing analysis.
Evidence references (relative to project root unless URL):
docs/dual-rocket/reports/synthesis/README.md
scripts/dual-rocket/synthesis/README.md

## Slide 18
MEMORY IMPLEMENTATION
SRAM adaptation was a separate task
Logical memories must be matched to available macro width, depth and write-mask behavior.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
18
Evidence: reports/synthesis/README.md | reports/synthesis/inventory.json
7
interface shapes
16
logical memory instances
194
512 x 64 SRAM macros
Two-core-specific change
L2 directory: 1024 x 144 bits
Mask granularity: 18 bits
Adapter comparison result
7 interfaces x 3 seeds
212,364 compared cycles: PASS
Finite initialized-state simulation passed. Formal and X-state equivalence were not established.
Notes: Seven distinct generated SRAM interfaces represent 16 logical full-SoC bulk-memory instances. The adapter maps them into 194 fakeram45_512x64 macros (512 words by 64 bits each). Logical capacity is 5,958,656 bits; physical macro capacity is 6,356,992 bits, including padding and mapping overhead. This is not just architectural cache data. The dual-core directory is 1024 by 144 with 18-bit mask granularity; the one-core directory was 1024 by 136 with 17-bit granularity. Wrong widths, mask lanes and a missing instance were rejected by metadata negative controls. All seven interface tests passed three seeds and 212,364 compared cycles. These are finite initialized-memory comparisons, not formal equivalence, X-state proof or full mapped-SoC simulation.
Evidence references (relative to project root unless URL):
docs/dual-rocket/reports/synthesis/README.md
docs/dual-rocket/reports/synthesis/inventory.json

## Slide 19
RESULTS | SYNTHESIS
Synthesis results: mapped and linked
Exploratory Nangate45 / fakeram45 library estimate. Not die area or manufacturing signoff.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
19
Evidence: reports/synthesis/README.md | reports/synthesis/mapped-statistics.json
383,763
total mapped instances
383,569
standard cells
194
SRAM macros
4.004733 mm²
total Liberty cell-area sum
SRAM: 3.356479 mm² (83.8%)
Standard cells: 0.648254 mm²
55,694 flip-flops + 1 latch are included in standard cells. Unmapped cells / memories / processes: 0.
Notes: The fresh run completed September 6, 2026. Yosys maps 383,569 standard cells including 55,694 flip-flops and one DLL_X1 latch, plus 194 SRAM macros for 383,763 total instances. No unresolved internal cells, Yosys memories or processes remain. OpenROAD independently links every instance. Total Liberty cell area is 4,004,732.942001 square micrometers; SRAM subtotal is 3,356,478.972 and standard-cell subtotal 648,253.970001. Divide by one million for square millimeters. These are sums of library areas without a floorplan, not die/core area, utilization or timing. The Nangate45/fakeram45 platform is exploratory and non-manufacturable.
Evidence references (relative to project root unless URL):
docs/dual-rocket/reports/synthesis/README.md
docs/dual-rocket/reports/synthesis/mapped-statistics.json

## Slide 20
LIMITS AND RISKS
What is not proven yet
Successful elaboration, tests and mapping are milestones, not chip signoff.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
20
Evidence: SOC.md | reports/simulation/README.md
AREA
REMAINING WORK / BOUNDARY
Clock and timing
500 MHz is nominal intent, not achieved CPU frequency.
Physical design
No placement, routing, power analysis or DRC/LVS.
Functional closure
No exhaustive coherence, formal proof or coverage percentage.
Software / debug
Linux boot and full JTAG/OpenOCD workflows not tested.
Serial and reset
Heavy-traffic serial-PHY warning; reset-domain review needed.
Mapped behavior
No full-SoC SRAM-mapped gate-level regression.
Report the design as a verified experiment with explicit limits, not a production-ready ASIC.
Notes: The nominal 500 MHz bus configuration and 500 kHz DTS timebase are not measured silicon clocks. CPU clock-frequency fields are zero. No timing constraints, STA closure, placement, routing, power analysis, DRC/LVS or manufacturability claim was established. Linux boot, full JTAG/OpenOCD flows, exhaustive coherence, coverage percentages, formal verification and SRAM-mapped gate-level regression remain untested. Serial TileLink's selected decoupled PHY has a retained heavy-traffic deadlock warning; the generator recommends a credited PHY when deadlock freedom is required. Prior fast memory loading does not test sustained serial safety. Lint reset warnings need dedicated review.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/reports/simulation/README.md
docs/dual-rocket/reports/lint/README.md
docs/dual-rocket/reports/synthesis/README.md

## Slide 21
NEXT EXPERIMENTS
How to try the next SoC configuration
Proposed work only. None of these changes is included in the current generated SoC.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
21
Evidence: CONFIGURATION.md | SOC.md
OPTION A: CORE / CACHE
Change core count or cache geometry.
Recheck coherence clients and SRAM shapes.
OPTION B: FFT ACCELERATOR
Integrate the optional generator.
Define interface and numerical tests.
Use a new named Config and preserve this baseline.
Regenerate RTL, device tree, memory map and SRAM inventory.
Add targeted software tests, then rerun lint and full-SoC synthesis.
Choose the workload first; compare new designs with the same tools and explicit acceptance criteria.
Notes: This is a proposed engineering sequence, not completed integration. For an FFT accelerator, first initialize and inspect the optional FFT generator at the pinned revision and study its integration rather than assuming the class exists in the main tree. Choose a documented attachment, addressing and interrupt scheme as applicable. New core/cache configurations change memory shapes and need refreshed adapters. Preserve the current experiment, use distinct config names and output roots, regenerate metadata, add feature-specific tests, and rerun lint/synthesis. Quantitative comparisons require common tools and constraints. No FFT hardware or Linux boot is claimed in the current design.
Evidence references (relative to project root unless URL):
docs/dual-rocket/CONFIGURATION.md
docs/dual-rocket/SOC.md
scripts/dual-rocket/README.md

## Slide 22
REPRODUCTION
Where the reproducible process lives
The results repository is not a complete toolchain or a vendored Chipyard checkout.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
22
Evidence: CONFIGURATION.md | scripts/dual-rocket/README.md
bash scripts/dual-rocket/generate.sh
bash scripts/dual-rocket/lint/run.sh
bash scripts/dual-rocket/synthesis/run.sh
Architecture + process
docs/dual-rocket/CONFIGURATION.md
docs/dual-rocket/SOC.md
Evidence + portable scripts
docs/dual-rocket/reports/
scripts/dual-rocket/README.md
Important: the top-level rtl/ folder is historical single-core RTL, not this dual-core build.
Notes: Run the commands from the results repository after provisioning the pinned Chipyard checkout and the documented EDA tools. CHIPYARD_ROOT, Java/RISC-V/PATH, OSS_CAD_SUITE_ROOT and ORFS_ROOT must be set as documented. generate.sh can reuse cached upstream output and requires exact source-manifest agreement. lint and synthesis use separate output roots and must not overwrite recorded attempts. The simulation evidence exporter only packages a completed campaign; it does not launch a simulator. The historical top-level rtl directory is single-core, while the dual-core hardware is identified by the generated-src DualRocketConfig path and its preserved hashes. Reports do not vendor raw large outputs, external libraries or binaries.
Evidence references (relative to project root unless URL):
docs/dual-rocket/CONFIGURATION.md
scripts/dual-rocket/README.md
docs/dual-rocket/README.md

## Slide 23
APPENDIX | VERSIONS
Pinned tools and source provenance
Versions describe the recorded experiment; this is not a recommendation to use arbitrary latest builds.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
23
Evidence: CONFIGURATION.md | reports/simulation/README.md
LAYER
RECORDED INPUT
Chipyard / Rocket Chip
e602d917dcc4 / 55bcad0f5943 (full SHA in notes)
Generator stack
Chisel 6.7.0; Scala 2.13.16; firtool 1.75.0
Java
OpenJDK 20.0.2-internal
RTL simulation
Verilator 5.022; DRAMSim2; matched Spike
Lint
Verilator 5.051 devel; slang 11.0.448
Mapping / memory checks
Yosys 0.68+195; ABC; Icarus Verilog 14.0 devel
Netlist link / libraries
OpenROAD v2.0-17598; pinned ORFS Nangate45 / fakeram45
476 RTL source hashes preserved; all 500 captured synthesis input hashes rechecked unchanged.
Notes: Exact full source revisions and dependency hashes are in the local references. Chipyard e602d917dcc495c58cabe906535e411707096c9c; Rocket Chip 55bcad0f59436de98ea510334121de8546b9e9d7; ORFS 68cc9bc974502b4786a68e9f51a092e0fcb56e82. Verilator simulator is 5.022, lint is 5.051 devel v5.050-312-gb1c06fdb0 (mod). slang is 11.0.448+e222e7dc0. Yosys reports 0.68+195 with a dirty suffix; native executable/plugin hashes are retained. OpenROAD v2.0-17598-ga008522d8. Icarus is version 14.0 devel s20260301-403-g5ab23063f-dirty. 500 synthesis input hashes were revalidated unchanged. Generation was not a clean dependency bootstrap and the later wrapper check was cached.
Evidence references (relative to project root unless URL):
docs/dual-rocket/CONFIGURATION.md
docs/dual-rocket/reports/simulation/README.md
docs/dual-rocket/reports/lint/README.md
docs/dual-rocket/reports/synthesis/tool-versions.txt
docs/dual-rocket/reports/synthesis/README.md
docs/dual-rocket/reports/workflow/README.md

## Slide 24
APPENDIX | READING GUIDE
Quick glossary and evidence guide
All slides have speaker notes with project-relative source references.
DUAL ROCKET / CHIPYARD / EVIDENCE: 06 SEP 2026
24
Evidence: SOC.md | CONFIGURATION.md
TERM
MEANING IN THIS PROJECT
SoC / hart
Integrated system / one hardware execution thread
RTL / Config
Hardware description / generator parameter composition
L1 / L2
Private per-core caches / shared inclusive cache
TileLink / AXI4
On-chip fabric / external-memory interface
CLINT / PLIC
Timer + software interrupts / device interrupts
Start reading: docs/dual-rocket/README.md
Bottom line: two Rocket cores, one complete SoC, reproducible evidence and clearly stated limits.
Notes: Glossary: SoC is a system on chip. A hart is a hardware execution thread; this design has one hart per Rocket core. RTL describes digital hardware behavior. TileLink is the on-chip interconnect protocol used here; AXI4 is the external-memory interface. L1 is private to a tile; L2 is shared. CLINT supplies timer/software interrupts; PLIC routes device interrupts. Lint, simulation, synthesis and physical signoff are distinct. The companion slide manifest and speaker-notes Markdown contain all references and SHA-256 fingerprints of the cited local source files. Read the detailed reports for exact test identities, warnings, provenance and limitations. This deck is a derivative explanation and does not replace the raw evidence.
Evidence references (relative to project root unless URL):
docs/dual-rocket/SOC.md
docs/dual-rocket/CONFIGURATION.md
docs/dual-rocket/reports/simulation/README.md
docs/dual-rocket/reports/lint/README.md
docs/dual-rocket/reports/synthesis/README.md